## Slide 1: Introduction to Bioimage Analysis
Thursday 30 Mar 2023
Jitender
Marielle
informatics@jic

## Slide 2: Agenda
10:00 Start and Introduction
Overview
Concepts
11.15 am Coffee
Exercises
3:00pm Coffee

## Slide 3: Content
General Introduction
Core concepts in bioimage analysis and interpretation
Introduction to image formats and conversion
Pre-processing: cropping, correction, and filtering
Image segmentations methods with hand-on exercises
Lunch Break
eMeasurement and Phenotype classification using intensity and spatial information
Case studies: highlighting morphological metrics that can be extracted from images
Quick detour to supervised machine learning based classifying (phenotypes) in images.
Best Practices and discussion

## Slide 4
https://github.com/gitbackspacer/bioimage

## Slide 5: Material
http://training.scicomp.jic.ac.uk/docs/bioimaging_course_book
http://training.scicomp.jic.ac.uk/docs/advanced_image_analysis_book
\\jic-hpc-data\Project-Scratch\training\image-analysis-course\PPT
https://www.unige.ch/medecine/bioimaging/files/3714/1208/5964/CellCounting.pdf
https://cildata.crbs.ucsd.edu/media/images/36420/36420.tif
https://imagej.github.io/presentations/fiji-introduction/#/8
https://monashmicroimaging.github.io/gitbook-fiji-basics/demonstration_images.html
https://rawgit.com/JeremyPike/image-analysis-with-fiji/master/ImageAnalysisWithFijiSlides.pdf

## Slide 6: Introduction
Biology is data driven
Primary source is images:
optical/Fluorescence imaging or electron, EM
MRI
From collection of images
Suitable image to show a property
“Process to extract Quantitative data”: tools, techniques and Pitfalls
Data

## Slide 7: From microscope to data
“Maximising information capture”
Source: https://bioimagebook.github.io/chapters/3-fluorescence/1-formation_overview/formation_overview.html
Photon to Pixels
pixel values in a fluorescence image depend upon “numbers of detected photons”
Images cant be perfect: blurred and noisy

## Slide 8
“most that the image can tell us is how much light was emitted from any particular point from a sample”
infer
Presence feature, about the size and shape of a structure or relative concentration of a molecule.

## Slide 9: Pixel values being stored in a digital image
“Photon hits”

## Slide 10: LUT: change the appearance of an image without changing its pixel values.

## Slide 11
https://www.youtube.com/watch?v=2KF8vBrp3Zw

## Slide 13: Basics

## Slide 26: Processing and Analysis

## Slide 27: Maximising information capture
Sufficient resolution in spatial and/or temporal dimensions:
e.g. cell divisions Frequency of capture high enough
Sufficient range in spatial and temporal dimensions;
multiple images of the same sample in different position and experiment last long enough
Sufficient dynamic range to capture values of interest:
Intensity ranges in images: Intensity ranges in images

## Slide 28: Microscope files
Zeiss microscopes produce .lsm files
Leica microscopes: .lif.
Effectively a single microscope file contains multiple two dimensional images.
Confocal microscope data tends to be organised as follows:
One or more time series (often denoted by T)
One or more channels (often denoted by C)
One or more data series (often denoted by S)
Z stacks (vertical height data, denoted by Z)

## Slide 29: Reading formats
Restrictive Manufacturer’s software
Problem of the wide range of alternative formats for imaging data, a group of scientists and software developers created a library (a set of software tools) for managing life sciences image file formats.
Bio-formats
Bio-Formats is a standalone library or tool for reading and writing life sciences image file formats. It is capable of parsing both pixels and metadata for a large number of formats, as well as writing to several formats.

## Slide 30: ImageJ and Fiji (https://imagej.net/)
ImageJ Java free and open source program for working with images.
It was originally developed at the US NIH It is designed to be easily extensible, so that people can write plugins to extend its functionality.
Due to it’s popularity, there are a very wide range of plugins available, making it extremely useful for image processing. These plugins include the ability to load files through Bioformats, thus enabling ImageJ to handle microscope files.
Fiji (short for Fiji Is Just ImageJ) is a bundle containing ImageJ, the Java components needed to run it, and a collection of useful plugin

## Slide 31: Image measurements
Extracting quantitative data
Distance measurements
Intensity measurement (presence of a tagged substance (a protein) that we’re interested in)
Counting objects (number of cells in an image)
Segmenting : common segmentation algorithm is the watershed algorithm. Fiji includes a wide range of segmentation algorithms

## Slide 32: Processing images
Images might be noisy, focus might not be accurate, the image might be under- or over-exposed and so on.
Often we can compensate for some of these problems with image capture by later processing.
Lossless versus lossy operations (operation is not reversible) smoothing and sharpening

## Slide 33: Processing images
Edge detection; feature detection, enhance the visibility of edges within an image. Help further processing of the image, trying to perform operations that depend on recognition of cell wall (such as segmentation).
Removing noise; slightly noisy in image capture, we remove remove pixel noise using Gaussian blur or filter
Effectively this averages the value of each pixel with its neighbours, causing it to be ‘spread out’.

## Slide 34
Changing intensities
Optical capture devices have a dynamic range, which is the range of light intensities over which they can capture data.
Careful selection of the dynamic range allows to achieve the best either too “bright” or “dark”.
Thresholding, two values in which one value indicates the presence of signal and the other its absence

## Slide 35: Errors and imprecisions
most photons do not reach/register the detector
Uncertainty in space; light originating from a particular point cant be a single point focus:
end up being spread over several pixel “Blur”
Uncertainty in brightness
random variations in brightness everywhere throughout the image

## Slide 36: Blurry and Noisy
blur can cause us to misjudge the size of something by several hundred nm
https://bioimagebook.github.io/chapters/3-fluorescence/2-formation_spatial/formation_spatial.html

## Slide 37: Sandy photons
https://bioimagebook.github.io/chapters/3-fluorescence/2-formation_spatial/formation_spatial.html
Blurrrrr
apparent size,
intensity (brightnesses) and number of structures
Well understood 

## Slide 38: Mass processing of data Fiji
script the analysis of our data using Fiji’s internal scripting system.

## Slide 39: Exercise: Images as numerical data
Loading an image
We’ll start with one of the sample images in Fiji. Load the gel image by navigating through the following menu options:
File -> Open Samples -> Gel
Then save it as a “text image” as follows:
File -> Save As -> Text image
Try opening the file in a text editor. What do you see?
Visualising the image
http://training.scicomp.jic.ac.uk/docs/bioimaging_course_book/exercise-images-as-data.html

## Slide 40: Image Segmentation with Fiji
Filter
Segment
Analysis

## Slide 41: Counting

## Slide 42: Duplicate

## Slide 43: Make a copy of Original sample Image
Renamed to blob-J.gif

## Slide 44: Renamed to blobs-J.gif

## Slide 45: Cell counting/Segmentation
Highlight blob-J.gif and Edit/Invert
White low
Dark High values in the inverted blob-J.gif

## Slide 46: Image/Adjust/Auto Threshold

## Slide 47: Threshold: Otsu

## Slide 48: Analyze/Analyse Particles

## Slide 49: Analyze/Set Measurements

## Slide 52: Protocol
Make duplicate copies (1) named blobs-O.gif (2) blobs-W.gif

## Slide 53: Image/Adjust/Redirect to:

## Slide 57: https://www.unige.ch/medecine/bioimaging/files/3714/1208/5964/CellCounting.pdf

## Slide 58
https://rawgit.com/JeremyPike/image-analysis-with-fiji/master/ImageAnalysisWithFijiSlides.pdf

## Slide 59
https://rawgit.com/JeremyPike/image-analysis-with-fiji/master/ImageAnalysisWithFijiSlides.pdf

## Slide 60
https://rawgit.com/JeremyPike/image-analysis-with-fiji/master/ImageAnalysisWithFijiSlides.pdf

## Slide 61
https://rawgit.com/JeremyPike/image-analysis-with-fiji/master/ImageAnalysisWithFijiSlides.pdf

## Slide 62
https://rawgit.com/JeremyPike/image-analysis-with-fiji/master/ImageAnalysisWithFijiSlides.pdf

## Slide 63
https://rawgit.com/JeremyPike/image-analysis-with-fiji/master/ImageAnalysisWithFijiSlides.pdf

## Slide 64
https://rawgit.com/JeremyPike/image-analysis-with-fiji/master/ImageAnalysisWithFijiSlides.pdf

## Slide 65: Jupyter notebook

## Slide 72: Thanks
David Waters (Computing)
Abigail (Training)